## Slide 1: The Motion Recognition Algorithm Research --- Step Count Algomrith
Student: Jerry / Jie Sun
Tutor: Dr. Glavin, Frank
1.What is G-sensor and what is Step Algorithm?
2.How does G-sensor work?
3.Key Algorithms.
4.The demostration of my programme.
Catalogue:

## Slide 2: What is G-sensor?
A G-sensor is commonly referred to as an accelerometer. They are used in a wide range of devices like smart phones, vehicles.
Step Count Algorithm is a kind of algorithm which makes use of the G-sensor or other sensors put on human body to calculate how many steps the people walk or run.
What is Step Count Algorithm?

## Slide 3: How does G-sensor work?
When a pedestrian is walking on the road, the accelerometer will divide the motion acceleration by three directions, as we can see in the picture below: Vertical Direction, Forward Direction and Side Direction, which can be also called: X, Y and Z Axis.

## Slide 4
Analysis of Three Axes Accelerations
As we can see in the two pictures on the left, where a , h , g means horizontal acceleration, vertical acceleration and gravity force, respectively.
Notes: The strides of the walker are different according to the varying human parameters. The stride depends on several factors such as walking velocity, step frequency and the height of the walker etc.
The horizontal direction acceleration and vertical direction acceleration during the swing phase is denoted in equation below, where θ(t) is inclination angle of the leg at time t.

## Slide 5
Four kinds of algorithms:
Algorithm 1: Peak Detection Algorithm.
Algorithm 2: Transform Domain Algorithm.
Algorithm 3: Filtering Algorithm.
Algorithm 4: Pattern Recognition Algorithm.
Key Algorithms
Notes: This chart on the right shows the total acceleration wave of walking in pocket during 2 seconds from the 2.5 minutes above chart. From the diagram, we can mark some positive and negative peak values, and there are some rules for judging whether peak values are available or not:

## Slide 6
Positive Peak Choosing
1.Peak Detection Algorithm
Four Basic Conditions:
1. Current point is going down.(The Red Point)
2. The previous point is going up.(The Black Point)
3. At least going up twice before coming to positive peak.(The Red Point).
4. The value of the positive peak bigger than 1.2g
Chart: Accele Value
 | 3.3862 | 2.4353 | 1.5835 | 1.2846 | 1.5409 | 1.7205 | 1.681 | 1.7089 | 1.7887 | 1.8817 | 2.2212 | 2.8218 | 3.5316 | 4.0952 | 4.3803 | 3.9763 | 3.2525 | 2.3051 | 1.8139 | 1.9658 | 2.2525 | 2.2774 | 2.116 | 1.9344 | 1.5985 | 1.3974 | 1.5854 | 1.8291 | 2.2802 | 2.9697 | 3.552 | 4.0981 | 4.3408 | 4.1718 | 3.5811 | 2.7903 | 2.1418 | 1.9012 | 2.0514 | 2.0585 | 1.9043 | 1.9226 | 2.1434 | 2.4363 | 2.6005 | 2.7578 | 2.9428 | 2.9746 | 2.8299 | 2.6614 | 2.2913 | 2.1104 | 2.1372 | 1.9895 | 1.6779

## Slide 7
2. Transform Domain Algorithm
One Basic Condition:
1. The duration of two effective adjacent peaks must be longer than 0.2S.
Chart: Accele Value
Deleting the interference signal
Notes: Here the diagram shows the data caught in 50Hz, 0.02s Period, So if the numbers of data between the two effective adjacent peaks less than 10, means the data is invalid. We judge it is an disturbing singal.

## Slide 8
Two Basic Conditions:
The current peak value minus the last valley value must be bigger than the threshold.
The Threshold is Dynamic and related with different walking patterns.
3. Filtering Algorithm
Dynamic Threshold Values

## Slide 9
4. Pattern Recognition Algorithm
Two Basic Conditions:
The current peak value minus the last valley value must be bigger than the threshold.
The Threshold is Dynamic and related with different walking patterns.
Chart: Accele Value
Walking and Running Patterns

## Slide 10
My Own Porgram
This is My Programme

## Slide 11
References:
1. Title: A Step, Stride and Heading Determination for the Pedestrian Navigation System
2. Title: Full-Featured Pedometer Design Realized with 3-Axis Digital Accelerometer. Neil Zhao